## Slide 1: EL9333 – Lab 4
Cing-Yu (Frank) Chu

## Slide 2: Objectives
Emulate a functional SDN network
Understand and get familiar with OVS
Understand and get familiar with controllers

## Slide 3: Writing a Controller
There are many choice for writing the controller,
  RYU (I will introduce this)
  Beacon
  POX
  NOX
  etc…
When creating a mininet topology, use --controller remote

## Slide 4: RYU
Python based framework
Reference:
  http://osrg.github.io/ryu/
  http://osrg.github.io/ryu-book/en/html/
To install RYU
  use pip: pip install RYU (recommended)
  from source:
    git clone git://github.com/osrg/ryu.git
    cd ryu
    python ./setup.py install
Read the example provided in the reference to understand how to use RYU
  the simple_switch program will help

## Slide 5: Task in this Lab
Create the following topology using customized topology file
S1
S2
S4
S3
controller
H1
H2
H3
H4

## Slide 6: Task in this Lab
Enforce the following rules
  Everything follows shortest path
  When there are two shortest paths available
    ICMP and TCP packets take the lower/left path
      S1-S2-S3 and S2-S3-S4
    UDP packets take the upper/right path
      S1-S4-S3 and S2-S1-S4
  H2 and H4 cannot have HTTP traffic (TCP with port:80)
    New connections are dropped with a TCP RST sent back to H1 or H3
    To be more specific, when the first TCP packet (SYN) arrives S1 or S3, forwarded it to controller, controller then create a RST packet and send it back to the host.
  H1 and H4 cannot have UDP traffic
    simply drop packets at switches

## Slide 7: General Rule – ICMP & TCP

## Slide 8: General Rule – UDP

## Slide 9: Drop HTTP between H2 and H4
HTTP
TCP SYN
HTTP
TCP SYN

## Slide 10: Drop HTTP between H2 and H4
TCP RST
TCP RST

## Slide 11: Drop UDP between H1 and H4
UDP
drop
UDP
drop

## Slide 12: Hint!
Hard-coded ARP table (IP-MAC mapping)
  you can use --mac when creating the mininet topology, which may makes easier.
  let the controller reply to ARP request
When using addLink in your customized topology file
  you can use addLink(H1, S1, 1, 1) to specify the port number
Just assume the controller knows the topology already, and install some static/basic rule during the handshake between OVS and controller:
  ICMP and TCP packets on the upper/right path
  UDP packets on the lower/left path
  drop UDP between H2 to H3
For HTTP between H1 and H3
  install a rule on S1/S3 to forward TCP SYN to controller
  controller creates a TCP RST packet and send back to S1/S3
  S1/S3 sends TCP RST to H1/H3

## Slide 13: RYU – Simple Learning Switch

## Slide 14: Feature Handler
MAC-Port Mapping
datapath.id : switch ID
empty match
output to controller
define the rule to be installed

## Slide 15: Packet-In
learn and record MAC-Port
decide output port
FLOOD or known port?
install new rule on switch (dpid)
send the packet out (back to switch)
packet header processing
visit the packet library
https://osrg.github.io/ryu-book/en/html/packet_lib.html
(you will need this to generate ARP and TCP RST)

## Slide 16: To Run Your Controller
First, start your Mininet with your custom topology
  sudo mn --custom your_topo.py --topo mytopo --mac --switch ovsk --controller remote
Configure OpenFlow version on the switch
  ex: ovs-vsctl set Bridge s1 protocols=OpenFlow13
  set switch 1 to OpenFlow v1.3
Run RYU controller
  ryu-manager --verbose your_controller.py
  verbose: allow the controller to print out more info